## Slide 1
New Iron Catalyst Boosts Ammonia Production
Modern Catalyst Breakthrough in the Haber Process
ASE Resource Online

## Slide 2: Modern Iron Catalyst boosts the Haber Process
The Haber process produces ammonia (NH3) for fertilisers.
Improving the efficiency and yield per catalyst volume has been challenging.
Scientists have developed a new iron-based catalyst for making ammonia. Unlike the traditional Haber catalyst, this one has large iron particles coated with aluminium hydride (AlH₃) and potassium (K).
More info : Article: Improving ammonia synthesis: New iron-based catalyst surpasses century-old benchmark
N2
H2
Fe
AlH
Enhanced electron donation at Fe surface  better N2 cleavage
Inverse structure: metallic Fe particles with AlH
It produces 3× more ammonia per reactor volume.
Works well at lower temperatures (50–200 °C) compared to the usual 450 °C.
More efficient and sustainable, with lower energy use and less CO₂.
NH3
Notes: Additional notes
Catalysts & Promoters
Students learn that the Haber Process uses an iron catalyst promoted by substances like aluminium oxide and potassium oxide to break the strong N≡N bonds (rate‑limiting step).
This new catalyst follows the same principle but is optimised in structure: the AlH–K layer essentially acts as a promoter, enhancing electron flow and increasing active sites for N₂ splitting.
2. Temperature, Rate & Equilibrium
A key GCSE concept is that lower temperatures favour equilibrium yield but slow the reaction rate, so a compromise temperature (~450 °C) is used.
This new catalyst challenges that trade-off, achieving high rates even at much lower temperatures (50–200 °C)—this illustrates how better catalyst design can shift real-world industrial conditions.
GCSE Chemistry Links (AQA Spec 4.1.10.4 Haber Process, Edexcel Spec 4.86, 5.19C, 5.21C Reversible reactions and dynamic equilibrium, OCR Spec Gateway C6.1d, C6.1g, OCR 21st Century C6.4 Chemicals on industrial scale)
A level Chemistry Links (AQA Spec 3.2.5.6 Catalysts, OCR Spec 3.2.3 Chemical equilibrium)

## Slide 3: Modern Iron Catalyst vs traditional Haber Process
 | Haber Process | Modern Catalyst
Catalyst | Iron with Al2O3 and K2O | Iron with promoters (AlH, K)
Reaction conditions | 450 oC | 50 – 200 oC
Efficiency and sustainability | Higher temperature and pressure to maintain output = less sustainable | Less energy = less fossil fuel use and CO2 emissions
Reactions | Reversible, lower temperatures for better yield but slower rate | Faster rate without needing high temperatures

## Slide 4: Modern Iron Catalyst boosts the Haber Process
The Haber process produces ammonia (NH3) for fertilisers.
Improving the efficiency and yield per catalyst volume has been challenging.
Scientists have developed a new iron-based catalyst for making ammonia. Unlike the traditional Haber catalyst, this one has large iron particles coated with aluminium hydride (AlH₃) and potassium (K).
It produces 3× more ammonia per reactor volume.
Works well at lower temperatures (50–200 °C) compared to the usual 450 °C.
More efficient and sustainable, with lower energy use and less CO₂.
 | Haber Process | Modern Catalyst
Catalyst | Iron with Al2O3 and K2O | Iron with promoters (AlH, K)
Reaction conditions | 450 oC | 50 – 200 oC
Efficiency and sustainability | Higher temperature and pressure to maintain output = less sustainable | Less energy = less fossil fuel use and CO2 emissions
Reactions | Reversible, lower temperatures for better yield but slower rate | Faster rate without needing high temperatures
N2
H2
Fe
AlH
Enhanced electron donation at Fe surface  better N2 cleavage
Inverse structure: metallic Fe particles with AlH
NH3
More info : Article: Improving ammonia synthesis: New iron-based catalyst surpasses century-old benchmark
Notes: Handout version

## Slide 5
www.ase.org.uk